## Slide 1: Enterprise Network Infrastructure Project
Designed & Implemented by:
Name | ID
Mina Estfanous | 21026681
Ahmed Mahmoud | 21020112
Abdallah Essam | 21040042
Mohamed Bakr | 21043984
Omar Osama Elnahass | 21040042
Instructor:
Eng. Ahmed El-Emam

## Slide 2: Project Overview
Our project focuses on designing a complete enterprise network.
Ensures secure communication between departments.
Supports routing, switching, servers, and firewall security.
Built using Huawei devices on eNSP

## Slide 3: Project Goals
Create a stable and scalable network.
Enable communication between all VLANs.
Secure the network using ACL + firewall rules.
Provide Internet access through ISP.
Automate IP assignment via DHCP.
Build a future-ready enterprise infrastructure

## Slide 4: Network Topology
3-Layer Hierarchy
Core Layer: CORE1, CORE2
Distribution Layer: Dist1, Dist2
Access Layer: ACC1, ACC2, ACC3, ACC4
Firewall + ISP Router
Server Farm + Client PCs

## Slide 5: VLAN Design
VLAN | Subnet Department
HR 10 | 192.168.10.0/24
IT 20 | 192.168.20.0/24
Management 30 | 192.168.30.0/24
Payroll 40 | 192.168.40.0/24
Servers 50 | 192.168.50.0/24
Backbone 99 | 192.168.99.0/24

## Slide 6: IP Addressing
VLAN interfaces on CORE1 & CORE2 act as gateways
Server VLAN uses static IP addresses
User VLANs rely on DHCP
Point-to-Point links use /30 networks

## Slide 7: Routing (OSPF)
OSPF Area 0 used across the network Configured between:
ISP ↔ Firewall
Firewall ↔ CORE1
CORE1 ↔ Dist1, Dist2
CORE2 ↔ Firewall
Benefits: Fast convergence ,Dynamic updates ,Loop prevention

## Slide 8: Switching Configuration
Trunk links between Core ↔ Distribution ↔ Access
Access ports assigned to correct VLANs
Spanning Tree enabled by default
Supports scalability and stability

## Slide 9: DHCP Configuration
DHCP server configured on CORE1
Pools created for: HR, IT, Management, Payroll, Servers
DHCP Relay enabled on Dist1 & Dist2 to forward DHCP requests
Ensures automatic IP assignment to all PCs

## Slide 10: Security (ACL Rules)
ACL used to:
Limit access between VLANs
Allow IT department admin access
Protect Management VLAN
Secure backbone VLAN
Applied on CORE1, CORE2, and Firewall

## Slide 11: Firewall Security
Policies created on FW-HQ:
Allow internal LAN → Internet
Allow OSPF updates
Control traffic to/from servers
Deny unauthorized access
NAT configured for Internet access

## Slide 12: Server Infrastructure
VLAN 50 includes:
Active Directory Server
DHCP Server (optional backup)
File Server
Monitoring (NMS)
Backup Server
All servers use static IPs.

## Slide 13: Testing & Troubleshooting
Tested | Fixed Issues
Ping between all VLANs | Wrong VLAN tagging
Routing table propagation | ACL blocking traffic
OSPF neighbor states | FW blocking ICMP
DHCP address assignment | DHCP relay not enabled properly
Firewall permit/deny rules | 
Internet access (8.8.8.8) | 

## Slide 14: Results
Fully functional enterprise network
Secure communication between departments
Internet connectivity for all VLANs
Centralized DHCP working
Routing stable via OSPF
Firewall policies applied correctly

## Slide 15: Conclusion
Project achieved all goals
Network is secure, scalable, and future-ready
Supports servers, users, and management
Demonstrates complete enterprise data-center design